# M-Link Data Layer
M-link data layer operates with words of 4 bytes width.
## Data Frame Format

Sync	Type	Length	Seq	Dst	Src	Data	CRC

field	offset	size	description
Sync	0	2	Sync word. 0x2A, 0x50 = “*P”
Type	2	2	Frame type
Length	4	2	Frame length in 32-bit words. Valid length is 4 – 511 (data size 0-507)
Seq	6	2	Frame sequence number (counter)
Dst	8	2	Destination Address
Src	10	2	Source Address
Data	12	0-2028	Payload data. 0-507 32-bit words
CRC	last	4	CRC32

Field offset and size in bytes.
Data flow: for each endpoint, SEND is what endpoint is sending
## Data Frame Types

type	description	data format
0x0100	Run mode data	application specific
0x0101	Register R/W request	Frame_101_102
0x0102	Register R/W response
0x0103	Status response	application specific
0x0105	RAM R/W request	Frame_105_106
0x0106	RAM R/W response
0x0107	Configuration EEPROM R/W request	Frame_107_108
0x0108	Configuration EEPROM R/W response
0x0110	FVME run mode data	VmeDaqRawdataFormat
0x0111	FVME request	Frame_111_112
0x0112	FVME response
0x1001	JTAG single op request	Frame 1001-1004
0x1002	JTAG single op reply
0x1003	JTAG shift 32 request
0x1004	JTAG shift 32 reply
0x5A5A	Loopback Test	any data
0x5354	Stream data	MStream

## Reserved Addresses

address	description
0xFEFE	point-to-point
0xFDFD	PCIe carrier board

MLink

# ADCM Raw Data Format
## Version 1.0
ADCM raw data has block structure. One or more data blocks are packed in M-Link frames with frame type 0x0100. Ignore other frame types, it is not ADCM data but special service data. Data block may not be fragmented, it should fit in one frame. Data block size should be multiple of 4 bytes.
Data block starts with the header word. Bits 26:31 contain data block ID and define the structure of the data block.
ID=0, ADC data
word	bits	width	description
0	3:0	4	Number of ADC bits (10-14)
	5:4	2	Number of samples per word = 2
	17:6	12	Number of samples (0-4095)
	25:18	8	Channel number (0..255)
	31:26	6	data block ID = 0
1	15:0	16	Event count
	31:16	16	Burst count
2	15:0	16	sample 1
	31:16	16	sample 2
...
n/2+1	15:0	16	sample n-1
	31:16	16	sample n
n/2+2	31:0	32	Event timestamp
n/2+4	31:0	32	constant

ID=1, ADC counters
word	bits	width	description
0	4:0	4	Number of words per channel
	12:5	8	Number of channels
	25:13	13	reserved
	31:26	6	data block ID = 1
1	31:0	32	hit count, channel 1
...
N	31:0	32	hit count, channel N
N+1	31:0	32	Event timestamp

ID=2, ADC data rev.2
word	bits	width	description
0	3:0	4	Number of ADC bits (10-14)
	5:4	2	Number of samples per word = 2
	6	1	Last fragment flag
	17:7	11	Number of samples in fragment / 2 (0-2047)
	25:18	8	Channel number (0..255)
	31:26	6	data block ID = 2
1	15:0	16	Event count
	31:16	16	Fragment number
2	15:0	16	sample 1
	31:16	16	sample 2
...
n/2+1	15:0	16	sample n-1
	31:16	16	sample n
n/2+2	31:0	32	Event timestamp
n/2+4	31:0	32	constant